## Slide 1: RRT for Quadrotor Motion Planning with Danger Zones in The Environment
Roya Sabbagh Novin, Dejun Guo
Shantnu Kakkar, Xiang He
Supervisor: Dr. Herman
Fall 2015

## Slide 2: Introduction
Quadcopters rescue in damaged structures
Flexibility, e.g., hover and fly in complex areas

## Slide 3: Project Definition
Map building: GUI + 3D environment
Path planning: RRT + cost + dynamic constraints
Path smoothing: Bspline

## Slide 4: Why RRT?
Fast for single query requirement. Give little bias and it will boooom. (PRM requires some additional steps)
Kinematic and dynamic constraints. (acceleration, velocity, etc.)
Collision checking is a separate independent module.

## Slide 5: Basic RRT
Drawbacks:
Danger zones
Constraints
Smoothness
*Choset, Howie; “Principles of Robot motion”

## Slide 6: Graphical user interface (GUI)
Different elements
Different shapes
Level of danger

## Slide 7: Danger Zones
A danger zone is an area with hazardous condition, i.e., heating, poor wireless networking, air flow, …
The path is allowed to intersect with the danger zones but this should be avoided as much as possible considering the level of danger.
The level of danger determines how much the area should be avoided.

## Slide 8: Cost function
No danger: d = norm(new_sample – n_i)
Low danger: 1.3*d
Medium danger: 1.4*d
High danger: 1.5*d

## Slide 9: RRT Constrained
Constraints:
Limit on acceleration
Limit on turning angle

## Slide 10: Path smoothing
It is a post processing tool to ensure that there are no abrupt changes in direction. (in other words, it ensures continuity of velocity, acceleration and radius of curvature)
RRT Constraint helps satisfy acceleration limits, but continuity is not ensured.
Method used: B-splines

## Slide 11: PATH SMOOTHING
Bsplines:
  local support. Re-positioning of path points & introducing pseudorandom points
  continuous (can go up to C3 continuity without increasing program complexity)
  No wobbling, curve within convex hull

## Slide 12: Path smoothing

## Slide 13: Developing map
Read image produced by the GUI
Use the RGB components produced in the image to know free space, obstacles, start, goal, etc.
Generate a txt file based on the RGB values.

## Slide 14: 3D environment
Used Open GL for 3d visualization
Used ROS for communicating. Two nodes are made, one of which reads the file containing the path. This node then passes position and attitude data to the other node (the open GL node).
Reading node
OPEN GL
Position
Attitude

## Slide 15: Final Result

## Slide 16: Conclusion
Method:
  Developed a GUI for user-friendly inputs
  Basic RRT + Cost function + Acceleration constraints
  Smoothing using B-splines
  Developed a 3D environment for better visualization
Results and future work:
  Find and smooth path considering the constraints and danger zones
  Considering narrow passages
  More realistic danger zones
  More complicated dynamic constraints

## Slide 17: References
D. Sent, M. H. Overmars. "Motion planning in environments with danger zones." IEEE International Conference on Robotics and Automation, ICRA. Vol. 2, 2001.
Choset, Howie M. Principles of robot motion: theory, algorithms, and implementation. MIT press, 2005.
Koyuncu, Emre, and Gokhan Inalhan. "A probabilistic b-spline motion planning algorithm for unmanned helicopters flying in dense 3d environments." Intelligent Robots and Systems, 2008. IROS 2008. IEEE/RSJ International Conference on. IEEE, 2008.

## Slide 18
Thanks For Your Attention! 

## Slide 19: Collision checking